## Slide 1
North Branch Reservoir
nbr_res_stor (storage)
nbr_res _withdr (withdrawal)
nbr_res _rel (release)
Prototype 1
Little Seneca Reservoir
seneca_res_storage
Seneca_res_release_spill
seneca_res _release_wq
seneca_res _release_ws
seneca_res_inflow_daily.csv
nbr_res_inflow_daily.csv
wma_demand_daily.csv
To represent flows from rest of Potomac watershed, use
lfalls_nat_daily.csv
potomac
lfalls gage
lag = 9 days
lag = 0 days
Key
Node
type = reservoir
Node
type = channel point
Stream channel
External inflow
External outflow
lfalls 9-day fc (from empirical algorithm used in PRRISM)
lfalls 0-day fc (ie known need at Little Falls)
The purpose of Prototype 1 is to practice simulating reservoir operations. The time step is daily. Lag times are constant. Demands are from a given time series. The forecast (fc) for the Seneca release is “perfect knowledge” of need.

## Slide 2
Prototype1 Narrative
Prototype1 is meant to be a very simplified version of the WMA water supply system that will get people going on how to simulate the basic operations of a reservoir. It has the following key features:
Time step: daily
Reservoirs
  Little Seneca
  “North Branch Reservoir” (NBr) – a fictitious combination of Jennings and Savage
Input time series: derived from PRRISM (From 1929-10-01 to 2013-12-31) (all mgd)
  lfalls_nat_daily.csv – Little Falls “natural flow” - without effects of reservoir watersheds & without WMA withdrawals
  nbr_res_inflow_daily.csv – NBr inflows (sum of Jennings & Savage inflows)
  seneca_res_inflow_daily.csv – Little Seneca Reservoir inflows
  wma_demand_daily.csv – a time series of total WMA daily demands that I output from PRRISM
Flow forecasts – we need Potomac River flow forecasts for Little Falls (“adjusted”, that is, flow before water supply withdrawals) to make water supply releases
  9-day flow forecast for NBr release – use the empirical equation we use in PRRISM – see Ahmed et al. (2015) Eq. 5-1, p. 5-5
  0-day forecast for L Seneca release – assume perfect knowledge, as we used to do in PRRISM, ie flow is today’s known Little Falls “adjusted” flow
Demand forecasts – for now just use the demands in the input demand time series
Reservoir operations: in prototype1 is simulating
  capacity – a constant
  storage – beginning of day (bop) storage volume
  flowby – minimum release for environmental purposes - a constant in prototype1
  ws_release: water supply release = need = demand + 100 – flow forecast
  inflow – from the daily inflow time series
  outflow – into the receiving stream
capacity
storage
Water balance equation for BOP storage on day i+1:
Subject to constraints:
storage i <= capacity
storage i >= 0
outflow i >= flowby, assuming there’s enough water
outflow i >= ws_release, assuming there’s enough water
storage i+1 = storage i + inflow i – outflow i